## Slide 1: Black Swans, White Swans and the Purple Transition
Simon P. Michaux
Associate Professor Mineral Processing & Geometallurgy

## Slide 2: Summary
Mapping the Green Transition
4 buffer sizes to manage intermittency of solar and wind power supply
Quantity of metals needed
  Compared to global annual mining production 2019
  Compared to mineral reserves, resources and under sea resources
Make batteries of something other than lithium-ion chemistry
The commodities industry has been misunderstood
Liquid fuel fission using thorium as the fuel
Ammonia fueled ICE
The Purple Transition

## Slide 5
Table 43. Total metal quantity required to phase out fossil fuels, by different buffer for stationary power storage capacity
6 hours (Larson et al 2021)
Larson, E., Greig, C., Jenkins, J., Mayfield, E., Pascale, A., Zhang, C., Drossman, J. Williams, R., Pacala, S., Socolow, R., Baik, E.J., Birdsey, R., Duke, R., Jones, R., Haley, B., Leslie, E., Paustian, K., and Swan, A., (2021): Net Zero America: Potential Pathways, Infrastructure, and Impacts, Final Report Summary, Princeton University, Princeton, NJ, 29 October 2021, https://netzeroamerica.princeton.edu/?explorer=pathway&state=national&table=e-positive&limit=200
48 hours +10% (Steinke et al 2012)
Steinke F., Wolfrum Ph., and Hoffmann C. (2012): Grid vs. storage in a 100 % renewable Europe. Renewable Energy, 50 (2013), 826-832
28 days (Droste-Franke 2015)
Droste-Franke, B. (2015): Review of the need for storage capacity depending on the share of renewable energies (Chap. 6). In Electrochemical energy storage for renewable sources and grid balancing. Netherlands: Elsevier
12 weeks (Ruhnau & Qvist 2021)
Ruhnau, O., and Qvist, S., (2021): Storage requirements in a 100% renewable electricity system: Extreme events and inter-annual variability, ZBW – Leibniz Information Centre for Economics, Kiel, Hamburg, https://www.econstor.eu/bitstream/10419/236723/1/Ruhnau-and-Qvist-2021-Storage-requirements-in-a-100-renewable-electricity-system-EconStor.pdf

## Slide 6
Remember, this is for just the first generation of units.
They will wear out in 10 to 25 years, after which they will need to be replaced
Mining production in 2019 (the last year of sensible data)
(USGS Mineral Statistics 2023)

## Slide 7
Reported Mineral Reserves + Estimated Resources + Undersea Resources
(USGS Mineral Statistics 2023, Hein et al. 2020)
Copper
Nickel
Cobalt
Lithium
Vanadium

## Slide 8: Make batteries out of something else
Zinc
Fluoride
Sodium
Magnesium
Most of these things can be found in industrial waste
The valuable part becomes processing and refining into something useful
A Circular Economy action

## Slide 9
The LFTR (2 MW) used in Circa Whuhai, China in 2022 – now commercially selling power
6000 hours power generation
Already done in China
The MSR used in the Oak Ridge Molten salt reactor (7.4 MW) commercial pilot 1969
ORNL (1972): The Development Status of Molten Salt Breeder Reactors, Report ORNL - 4812, Oakland Ridge Nuclear Laboratory, United States Atomic Energy Commission (AEC)
https://thethoriumnetwork.com/2022/05/03/%e3%83%91%e3%83%bc%e3%83%95%e3%82%a7%e3%82%af%e3%83%88%e3%83%86%e3%82%af%e3%83%8e%e3%83%ad%e3%82%b8%e3%83%bc-%e3%83%90%e3%82%a4%e3%83%aa%e3%83%b3%e3%82%ac%e3%83%ab%e8%a8%98%e4%ba%8b-%e6%97%a5%e6%9c%ac/
The status report outcome of billions of dollars and several decades of research and development (100 billion $USD in 2023 adjusted for inflation)

## Slide 10
10 000 GWh of electrical power is generated
(365 days)
1.45 tonne of natural ThO2 mined from approx. 280 tonne of monazite mineral sands (@0.5% grade Th)
1.34 tonne of 232Th in Thorium fluoride salt
96% Waste fuel SNF
Conversion of U3O8 to UF6 (347.9 tonne)
Nuclear fuel UO2 assembly fabrication
(32.9 tonne)
with 4.9% 235U
278.8 tonne of natural U3O8 mined from approx. 123 Mt of ore (@0.5% grade)
10 000 GWh of electrical power is generated
(365 days)
53.84 kg of contaminated fuel (LLW). Mostly medical isotopes (Xe, Ce, Sr, Zr, I, etc.)
Stored for 300 years if not recycled
Liquid Fuel Thorium Molten Salt Reactor
Uranium Light Water Reactor
https://www.wise-uranium.org/nfcm.html
THE THORIUM NETWORK
1-5% radioactive isotopes
Enrichment of UF6 235U @ 4.09% (43.3 tonne)
SNF (kg)
Can also run with a U salt mix, and with some SNF

## Slide 14: Copenhagen Atomics
Each commercial rector is planned to be able to produce 100 MW of thermal heat, or 40 MW of electricity
Each reactor is the size of a 40 foot shipping container
Electricity will be sold at a projected 2 cents/kWh
1g of thorium or uranium produces 24 MWh of thermal energy.
  A plant producing 1 GW electricity needs 800kg of Th232 metal in salt form each year.
First test of complete system to generate electricity in late 2025 to 2026
Commercial reactors will be available for sale in 2028 (at this stage)
Test rig with a full sized reactor to pilot test the water circuit
https://www.copenhagenatomics.com/

## Slide 15
https://www.autoracing1.com/pl/413299/toyota-ceo-our-ammonia-engine-will-be-the-end-of-evs/
The EV Black Swan is here
The sourcing of raw materials for manufacture drove this decision
The battery market will now crash (opinion)
Ammonia Fueled ICE – passenger vehicles to ships

## Slide 21: The commodities sector has been misunderstood
Energy
Economics
Minerals
Technology
Human Society
Each one of these aspects cannot be considered without the other three
All of these aspects and human society functions by harvesting feedstock from the planetary environment
This is how our system is really structured
Any new system will have to have a similar structure
Our relationship between all 4 aspects & the planetary environment is changing
Finance & Economics
Sometimes about technology

## Slide 22
Application
Generation
Electric Vehicles
Oil
Electricity
Manufacture
Coal
Gas
ICE
Petroleum
ICE
Ammonia
Hydrogen Fuel Cell
Biofuels
Transport
Nuclear
Wind
Geothermal
Hydro
Solar
Wave
Biowaste
Natural limitations to expansion
Buffer to manage intermittency
Can’t expand fast enough
To be phased out
Heat
Can we produce the ammonia from seawater?
Batteries
Limited supply of biomass
Limitations in storage and transport of H2
Liquid Fuel Fission Th MSR
U (LWR)
Exhaust gas?

## Slide 23: The Purple Transition
Application
Generation
Electricity
Manufacture
ICE
Ammonia
Transport
Heat
Liquid Fuel Fission Th MSR (5600C)
Combustion of iron oxide powder to produce high temperatures (18000C)

## Slide 24
Simon P. Michaux
Associate Professor Geometallurgy
Circular Economy Solutions
simon.michaux@gtk.fi
gtk.fi
Kiitos & Thank you